## Kelly KBL/KEB/KSL/KBS Controller RS232 Commands List

## Version 1.1

## Data Structure definitions

#define ETS_MAX_DATA_LEN  			16  //max length,can not be changed

typedef struct _T_Sync_Comm_Buff

{

unsigned char  command;

unsigned char  no_bytes;

unsigned char  data[ETS_MAX_DATA_LEN + 1];

}T_Sync_Comm_Buff;

Description: Data structure T_Sync_Comm_Buff are used by the controller with whole data length 19 bytes. A complete data sent to the controller or received from the controller include the command field, no_bytes field and the data field.Serial baud rate is 19200.

The command field indicates the operation. The controller response returns the same command value it received.

The no_bytes field indicates the number of bytes to be sent or received of the data buffer field, excluding the checksum byte.

The data buffer field includes two parts: valid data and the checksum. Before sending T_Sync_Comm_Buff type data, the ETS_TxMsg method make a checksum and place it at the valid data heels. After receiving a complete data from the controller, the ETS_RxMsg method will make a checksum and compare it with the checksum part in the receiving data buffer field.

Refer to implementation of ETS_TxMsg, ETS_RxMsg ,Please See Appendix B Programming Reference.

## Commands definitions

Command	ETS_GPIO_PORT_INPUT

no_bytes		1

data[0]		6

Controller response

no_bytes		1

data[0]		bit0		brake switch in

Bit1 	reverse switch in

Bit2		ACC switch in

Description: Getting current physical switch input status. 1 - active, 0 - inactive. ETS_GPIO_PORT_INPUT constants defined in Caldata.cpp.

Command	ETS_GPIO_PIN_INPUT

no_bytes		1

data[0]		5

data[1]		4

Controller response

no_bytes		1

data[0]		bit0	 	sensor A status

Description: Getting the current Hall sensor signal status.  1 - active, 0 - inactive.

ETS_GPIO_PIN_INPUT constants defined in Caldata.cpp.

Command	ETS_GPIO_PIN_INPUT

no_bytes		1

data[0]		5

data[1]		5

Controller response

no_bytes		1

data[0]		bit0	 	sensor B status

Description: Getting the current Hall sensor signal status.  1 - active, 0 - inactive.

ETS_GPIO_PIN_INPUT constants defined in Caldata.cpp.

Command	ETS_GPIO_PIN_INPUT

no_bytes		1

data[0]		1

data[1]		0

Controller response

no_bytes		1

data[0]		bit0	 	sensor C status

Description: Getting the current Hall sensor signal status.  1 - active, 0 - inactive.

ETS_GPIO_PIN_INPUT constants defined as in Caldata.cpp.

Command	ETS_FLASH_OPEN

no_bytes		0

Controller response

none

Description: Copying flash data to ram before flash data reading operation.

ETS_FLASH_OPEN constants defined as in Caldata.cpp.

Command	ETS_FLASH_READ

no_bytes		3

data[0]		INFO_MODULE_NAME

data[1]		8

data[2]		0

Controller response

no_bytes		8

data[0]~data[7]	Controller’s model. in ASCII format, 8 bytes.

Description: Getting controller’s model no.

ETS_FLASH_READ constants defined in Caldata.cpp.

INFO_MODULE_NAME constant is defined in Caldata.cpp.

Command	ETS_FLASH_READ

no_bytes		3

data[0]		INFO_SOFTWARE_VER

data[1]		2

data[2]		0

Controller response

no_bytes		2

data[0]~data[1]	software version in BCD alike format, two bytes.

Description: Getting controller’s software version,  it also defined as the controller’s version, BCD alike format storage. E.g. 0x0A,0x01 should be parsed to ASCII characters ‘0’ ‘A’ ‘0’ ‘1’ as the software version. INFO_SOFTWARE_VER constant is defined in Caldata.cpp.

Command	ETS_FLASH_READ

no_bytes		3

data[0]		CAL_TPS_DEAD_ZONE_LOW

data[1]		1

data[2]		0

Controller response

no_bytes		1

data[0]		TPS_Dead_Zone_Low

Desccription:Getting controller’s Throttle low-end dead zone.

CAL_TPS_DEAD_ZONE_LOW constant is defined in Caldata.cpp.

Command	ETS_FLASH_READ

no_bytes		3

data[0]		CAL_TPS_DEAD_ZONE_HIGH

data[1]		1

data[2]		0

Controller response

no_bytes		1

data[0]		TPS_Dead_Zone_High

Desccription:Getting controller’s Throttle high-end dead zone.

CAL_TPS_DEAD_ZONE_HIGH constant is defined in Caldata.cpp.

Command	ETS_FLASH_READ

no_bytes		3

data[0]		CAL_BRAKE_DEAD_ZONE_LOW

data[1]		1

data[2]		0

Controller response

no_bytes		1

data[0]		Brake_Dead_Zone_Low

Desccription: Getting controller’s Brake low-end dead zone.

CAL_BRAKE_DEAD_ZONE_LOW constant is defined in Caldata.cpp.

Command	ETS_FLASH_READ

no_bytes		3

data[0]		CAL_BRAKE_DEAD_ZONE_HIGH

data[1]		1

data[2]		0

Controller response

no_bytes		1

data[0]		Brake_Dead_Zone_High

Desccription: Getting controller’s Brake high-end dead zone.

CAL_BRAKE_DEAD_ZONE_HIGH constant is defined in Caldata.cpp.

Command	ETS_A2D_BATCH_READ

no_bytes		0

Controller response

no_bytes		16

data[0]		Brake A/D

data[1]		TPS A/D

data[2]		motor temperature A/D

data[3]		Control power A/D

data[4]		Vs A/D

data[5]		B+ A/D

data[6]		Controller’s temperature A/D

data[7]		Ia A/D

data[8]		Ib A/D

data[9]		Ic A/D

data[10]		Va A/D

data[11]		Vb A/D

data[12]		Vc A/D

data[13]		H_Temperature

data[14]		V+ A/D

data[15]		L_Temperature

Description: Data batch reading.

- For control power, B+, Va, Vb, Vc, A/D value and voltage mapping relation is:

V = Vad / 1.84. (For 120V controller).

V = Vad / 1.39. (For 144V controller).

- Vs is defined as the 5V power supply for Hall sensor, control panel,ect. A/D value and voltage mapping relation is: 0 ~ 127 mapping to 0 ~ 5V.

- Brake and TPS are defined as the Brake and the Throttle analog input. A/D value and voltage mapping relation is: 0 ~ 255 mapping to 0 ~ 5V.

- V+ is defined as the internal voltage of the controller. A/D value and voltage mapping relation is: 153~250 mapping to 9~15 V.

5)  motor temperature A/D is defined as the temperature of motor A/D 		   value.

6)  data[6],data[13],data[14] are defined as controller inside temperature 	   A/D value.

Command	ETS_MONITOR

no_bytes		0

Controller response

no_bytes		13

data[2]		Controller’s temperature

data[3]		B+ A/D

data[4]		TPSx A/D

data[5]		BRAKEx A/D

data[7]		I A/D

data[8]		zero current A/D

data[9]		MSB of controller’s error state

data[10]		LSB of controller’s error state

data[11]		MSB of mechanical speed in RPM

data[12]		LSB of mechanical speed in RPM

Description: Data batch reading.

- data[0] and data[1] are not supplied.

- data[2] is defined as the temperature of the controller in Celsius temperature.

- TPSx – Valid range of TPSx is [0, 200].

- BRAKEx – Valid range of BRAKEx is [0, 100].

- I A/D defined as the phase current A/D value.

- Controller error status：(data[9] << 8) | data[10],

| data[9]M | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | data[9]L |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0x44 | 0x43 | 0x42 | 0x41 | 0x34 | 0x33 | 0x32 | 0x31 |  |
| data[10]M | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | data[10]L |
|  | 0x24 | 0x23 | 0x22 | 0x21 | 0x14 | 0x13 | 0x12 | 0x11 |  |

if(data[9] << 8) | data[10]=0x4008,The corresponding error code is 0x43and 0x14.

- Mechanical speed calculation: (MSB << 8) | LSB. If the speed out data is not match the real speed value, please configure the motor poles calibration data of the controller based on the driven motor.

Command	ETS_INVALID_COMMAND

Controller response

Command	ETS_INVALID_COMMAND

Description: Invalid command.

Appendix A: Caldata.cpp

ETS_GPIO_PORT_INPUT				0x1E

ETS_GPIO_PIN_INPUT				0x1F

ETS_FLASH_OPEN					0xF1

ETS_FLASH_READ					0xF2

ETS_A2D_BATCH_READ				0x1b

ETS_MONITOR						0x33

ETS_INVALID_COMMAND			0xE3

INFO_MODULE_NAME				0x40

INFO_SOFTWARE_VER				0x53

CAL_TPS_DEAD_ZONE_LOW		0x04

CAL_TPS_DEAD_ZONE_HIGH		0x26

CAL_BRAKE_DEAD_ZONE_LOW		0x05

CAL_BRAKE_DEAD_ZONE_HIGH	0x27

ETS_FLASH_INFO_VERSION        0xFA

OPEN_LEVEL 						0

CLOSE_LEVEL						1

Appendix B : Programming Reference

- RS232 command sending and receiving samples

CommClass	m_Comm;	//Object of CommClass

  - Connection

//Connect to the controller

errorcode = m_Comm.ComOpen(pBuffer);

if(errorcode != COMM_ERROR_OK)

{

//error dealing

}

else

{

//operation on connection success

}

  - Data sending/receiving sample – ETS_FLASH_OPEN

//data sending/receiving with retry-on-fail

while(errorcode != COMM_ERROR_OK && readloopcount-- > 0)

{

m_Comm.m_SyncOutputBuff.command = ETS_FLASH_OPEN;

m_Comm.m_SyncOutputBuff.no_bytes = 0;

errorcode = m_Comm.ComSyncSend();	//send data using internal buffer

}

if(errorcode != COMM_ERROR_OK)

{

//error dealing

}

else

{

//operation on connection success

}

  - Data sending/receiving sample – ETS_FLASH_READ

m_Comm.m_SyncOutputBuff.command = ETS_FLASH_READ;

m_Comm.m_SyncOutputBuff.no_bytes = 3;

m_Comm.m_SyncOutputBuff.data[0] = INFO_SOFTWARE_VER;

m_Comm.m_SyncOutputBuff.data[1] = 2;

m_Comm.m_SyncOutputBuff.data[2] = 0;

errorcode = m_Comm.ComSyncSend();

if(errorcode != COMM_ERROR_OK)

{

//error dealing

}

else

{

//operation on connection success

}

- Notice on time delay setting

Controller’s Flash reading/writing operations need some time to finish, so it is necessary

to set longer receiving wait time using ComSetDelayTime method in CommClass.

3)  ETS_TxMsg和 ETS_RxMsg

T_Sync_Comm_Buff  Rx_Buff,TxBuff;	//define send and receive data buffer field

//transmit message

int ETS_TxMsg(void)		//calculate checksum and transmitter data

{

char i,check_sum;

check_sum = 0;

for (i=0; i<Tx_buff.no_bytes; i++)

check_sum += Tx_buff.data[i];

check_sum += Tx_buff.no_bytes;

check_sum += Tx_buff.command;

Tx_buff.data[Tx_buff.no_bytes] = check_sum;  //load checksum

WriteFile();//send

return 1;

}

int ETS_RxMsg(void)

{

unsigned char check_sum,k=0,i=0,len=0;

for(int j=0;j<10;j++)//receive 10 times

{

Sleep(5);//wait 5ms

len=0; //Number of bytes

ReadFile();//Read the serial port, the data storage into Rx_Buff, 									Rx_Buff.no_bytes given len

for (i = 0; i < len; i++)

{

check_sum += Rx_Buff.data[i];

}

check_sum += Rx_buff.no_bytes;

check_sum += Rx_buff.command;

if(check_sum !=Rx_Buff.data[Rx_buff.no_bytes])//checksum error

return 0;

else

return 1;	//OK

}

return 2;//don't receive data

}